# Determining Temperature from an ADC (Channel 0)

Reference:	Wikipedia: Thermistor, Electronics in Schools

This determination assumes that our NTC Thermistor (R1) is placed in series with a fixed 10kΩ resistor (R2). Using the concept of a voltage divider to the right, let Vref  be the reference voltage and A0 be the reading from Channel 0 of the ADC.

From the formula offered at Wikipedia, we derive,

Where, from the characteristics of our NTC Thermistor,

.

See Thermistor.xls for the data and graph.